# Ripple Counters
## Task 1: A 2-bit counter
In the last lab you should have built a simple 2 flip-flop circuit that counted backwards from 3 to 0. At its heart was the toggle flip-flop made from a D-type latch with its D input tied to its bar Q output.
The reason that it counted down was because it fed the Q output of one flip-flop to the positive edge triggered input of the next flip-flop. If we feed forward the bar Q instead, we can build a circuit that counts up instead of down.
a) With reference to the way that binary counting works (figure?), explain why this should work.
Each time the clock goes high, the flip-flop inverts its state. If we feed forward !Q, then the higher bit will change state only when the lower bit changes from 1 to 0 (and so its !Q changes from 0 to 1). This corresponds to a time when we would be carrying a 1, so we get a sequence counting up.

Begin by connecting two D-type flip-flops in this way ( bar Q output of FF-1 to clock input of FF-2) and verify that they form a 2-bit counter. Drive the clock of the first flip-flop from the TTL output of your Designer set at 1Hz or slower signal and connect the two Q outputs to two of the LEDs on your Designer. Ignore the Q outputs.
b) Draw the circuit that you have used.

c) Drive the counter with a 1kHz clock from the TTL/CMOS output of your Instek signal generator and observe the clock and the two outputs on your scope. Do NOT paste in this image. Instead, sketch a timing diagram (a sketch of what the outputs would look like if seen on a 4-channel scope) of the input and both outputs and label it to show that the outputs form a counting sequence.
(Each period of the clock is 1 second)

d) Which flip-flop produces the high-order bit and which the low order?
FF2 produces the high-order bit. This is because it gets carried into by FF1.

## Task 2: The 4-bit counter
This principle of cascading flip-flops, output-to-clock, produces counters called ripple counters because of the way information ripples along from one flip-flop to the next. Extend this principle to produce a 4-bit binary counter using the LEDs on your Designer as outputs. You will need to lower the clock frequency to about 2 Hz.
a) Write the sequence of states that you observe below and explain why they forma counting sequence.
The sequence of states I observed went like this: (first bit = last FF output, etc.)
0000 → 0001 → 0010 → 0011 → 0100 → 0101 → 0110 → 0111 → 1000 → 1001 → 1010 → 1011 → 1100 → 1101 → 1110 → 1111 → 0000 → …
This forms a counting sequence because these numbers are clearly counting up in binary.

b) You can make the output more readable using one of the seven-segment displays built into your Designer. Wire the four outputs of your counter to the four inputs of the leftmost display. What do you see and why?
I see the display count up from 0 to 9, then stop, and reset back to 0 after a short delay. This is because the 7-segment display in the designer doesn’t display hex digits.

### Task 3: Decade Counter
Using just flip-flops we can only make ripple counters that can count up to powers of 2 (4, 8, 16, etc.). To build counters that go through some other sequence, such as 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 0, 1, etc (a decade counter), we have to stop the sequence after it reaches the last value. We can do this with the aid of the Clear inputs on the flip-flops. When the clear input is brought low it pulls the output of the flip-flop to 0 regardless of the state of the other inputs.
a) Design a small combinatorial circuit whose output is 1 for all inputs less than $A and goes to 0 the first time the 4-bit number on the inputs reaches 0xA. Connect the output of that circuit to all the clear inputs.
HINT: The book shows how to do this with a 4-input gate but you only have 2-input gates. There is a simple solution using only 1 gate if you think carefully.
b) Draw your circuit.

c) Describe and explain the resulting behavior of your counter.
My counter counts up as usual until it reaches the first state in which O3 and O1 are high, which happens to be 0xA. Then, all of the Ffs’ clears get triggered, and the counter resets back to 0. Thus, we see a normal count up to 9, then a split second of 10, and then back to 0.