# Lab 10: Power Supplies 1
Figure 1
## The Transformer
I have provided you with a small power transformer attached to a mains lead. Be careful with it. You are unlikely to damage yourselves but you could get a mild shock if you are careless. Don’t touch the bare wires coming from the transformer when it is turned on and you will be quite safe. Connect up the red, white, and black wires from the transformer (or red-clear-black in some cases) to the inputs of your oscilloscope as shown in Figure 1 on the right.
Make sure that your screen shows 2-3 periods of the signal and fill as much of the screen as possible. Paste an image of your screen in the box below.

a) Explain what you see. I want to know the magnitude and frequency of the voltages and to know what is the relationship between the two traces.
V1 is half of V2 because there are twice as many turns between ground and V2 as there are between ground and V1. Both signals’ frequencies are 60Hz, because this is the frequency of mains power. Vin and Vout are in phase because they are both on the same side of the ground lead.

b) Disconnect the oscilloscope and reconnect it as shown in Figure 2. Repeat the measurement and paste an image in the box below.
Figure 2

### b) Explain why the new image makes sense and explain how it makes sense that a single transformer could produce two such different images.
Since Vin and Vout are on opposite sides of the ground lead, we expect them to be 180° out of phase. Since there are an equal number of turns between Vin and ground as there are between Vout and ground, we expect the two signals to have the same amplitude.
## Full-wave Rectifier
Figure 3
Connect two diodes to the transformer to make a full-wave rectifier as shown in Figure 3. Connect one oscilloscope probe across the 270Ω 5W load resistor and the other to point a. DON’T plug the transformer in until I have checked your circuit!
Once your circuit is functioning adjust your scope to give a good view of the signals and paste a picture in the box below.

c) Measure and account for the peak voltage that you observe at the output.
The peak voltage is 10.2V. This implies a .8V drop across the diode.

Vout shows only the positive peaks from terminals `a` and `b` on the transformer, because the negative halves of the waves do not pass the diodes.

Now adjust the scales (and possibly the triggering) on your oscilloscope to show the detail of what happens in the region where the input voltage passes through 0. You want the total range to be about ±1 and 2-4 ms in duration. Paste the new image below.`

d) Discuss the shape of the output and account for the small flat region at 0V in as much detail as you can.
The small flat region is caused by the diodes. When the voltage is below the diode’s threshold, the diode won’t conduct, even if the current would flow in the correct direction.
## Smoothing
Return your oscilloscope to the settings for part c and then connect a 1000 µF capacitor in parallel with the 270 Ω load resistor. NOTE: The capacitor is polarized—it has a positive and a negative side. Please connect it up correctly because I don’t have many spares! Paste an image of the resulting screen in the box below.

e) Describe how the output voltage is now different and explain how the capacitor acts to cause this difference.
The output voltage is now a pretty steady 9.3V DC. This is because the capacitor stores charge until the voltage drops below 9.3V, at which point the capacitor discharges until the next peak.

f) What is the average current through the 270Ω resistor?
Since we have a DC voltage of 9.30V, this is just V=IR.
Thus, I = 9.30/270 = .0344A.

Expand the vertical scale and paste and image of the ripple voltage in the box below.
Hint: you may want to experiment with the AC coupling setting on that channel your scope.

g) What is the peak-to-peak magnitude of the ripple voltage?
214mV.

h) What is the frequency of the ripple?
121.6Hz.

i) Given that the line frequency is 60Hz explain why the ripple frequency has the value that you found.
The ripple frequency is double the input frequency because the smoothing capacitor discharges once per

j) Connect a second 270Ω load resistor in parallel with the first, re-measure the output voltage and the output ripple magnitude.
Frequency: 119.7Hz
Peak-to-Peak Voltage: 372mV

k) What is the average current drawn from the power supply now?
Remember that the average current comes from knowing the average voltage and not from knowing the ripple voltage!
Average Voltage: 8.94V
Average Current: Vripple * 2 * f * C = .372 * 2 * 60 * .001 = 44.64mA

l) For each of the cases compare the measured ripple voltage with the theoretical figure,
Vripple =
  Iout
120×C
where C is the value of the smoothing capacitor in Farads, and Iout is the average output current, in Amperes, delivered to the load.
Vripple = (10.2 / 270) / (120 * .001) = 0.3148148148148148
Vripple = (10.2 / 135) / (120 * .001) = 0.6296296296296297

m) Comment on the accuracy of this formula .
This formula seems pretty inaccurate. This could be because our transformer’s output is not sinusoidal, and its peak voltage output is flattened because of the smoothing capacitor.
2) If time permits use your two different output voltages to compute the Thévenin equivalent of the power supply.
Time did not permit.