# Lab 15: LED Displays and Decoding with Arrays
We continue to turn LEDs on and off but in much more complex patterns. We will move to a pre-built LED display and study a technique to translate from one encoding (binary) to another (7-segment control) using Python sequences and the indexing operation.
## Driving the 7-segment LED with a computer
In your last computer lab you learned to drive individual LEDs using a ULN2803 octal switch (octal means that there are eight of them). For this lab I provided you with a pair of boards that combine a ULN2803 with some resistors (in another DIP package) and a 7-segment LED display. This latter is a set of eight LEDs (yes, I know that seven and eight are not the same, the eighth is the decimal point) arranged so that they are easy to form into numbers, as below

The figure on the right shows the physical layout as seen the viewer and the figure on the left tells you how the LEDs are connected to the pins on the package. Since your LED display is already built on the board with the driver you will not have to worry about this at the moment. What you need to know is that bit 0 on your board is connected to segment a, bit 1 to segment b, and so on, through bit 6 that drives segment g and bit 7 that controls the decimal point. Because we use a driver chip, a HIGH (1) value on the computer output will turn the corresponding LED ON. Note the driver is the same ULN2803 that you used in the last two labs.
NOTE: The pin numbers on the LED figure are pins on the underlying LED chip and have nothing to do with either the pins on your Feather or the pins on the LED boards.
### Task 1) Lighting up some LEDs
Connect one of your 7-segment displays to some of the I/O pins on your computer and test it with a program that flashes each bit in turn for about 0.3-1 seconds and then repeats. Paste the commented program below.
# Author: Ben Kallus
# Blinks each segment in a 7-segment display

import board
import digitalio
import time

pins = [board.SCL, board.D5, board.D6, board.D9, board.D10, board.D11, board.D12, board.D13]
dios = []

for pin in pins:
    dio = digitalio.DigitalInOut(pin)
    dio.direction = digitalio.Direction.OUTPUT
    dios.append(dio)

while True:
    for dio in dios:
        dio.value = True
        time.sleep(.5)
        dio.value = False
        time.sleep(.5)

## DisplayHex
Your next assignment is to write a Python function that is passed a single-digit number, which it then shows on the display in hex (0,1,2,3,4,5,6,7,8,9,A,b,C,d,E,F where the 6 has segment a on to distinguish it from b). This is basically an extension of the example from computer chapter 6.
## Task 2: Choosing the bit patterns
We start by building a truth table showing the bits to turn on and off in order to make the display light up the segments to show the desired hexadecimal digit. I have done the first one for you and you need to fill in the rest. You may wish to note that we conventionally use a mix of upper and lower case for the HEX digits, A, b, C, d, E, and F. I leave you to figure out why.

Digit	g	f	e	d	c	b	a	Binary/Hex
0	0	1	1	1	1	1	1	0b00111111 or 0x3F
1	0	0	0	0	1	1	0	0b00000110 or 0x06
2	1	0	1	1	0	1	1	0b01011011 or 0x5B
3	1	0	0	1	1	1	1	0b01001111 or 0x4F
4	1	1	0	0	1	1	0	0b01100110 or 0x66
5	1	1	0	1	1	0	1	0b01101101 or 0x6D
6	1	1	1	1	1	0	1	0b01111101 or 0x7D
7	0	0	0	0	1	1	1	0b00000111 or 0x07
8	1	1	1	1	1	1	1	0b01111111 or 0x7F
9	1	1	0	0	1	1	1	0b01100111 or 0x67
A	1	1	1	0	1	1	1	0b01110111 or 0x37
b	1	1	1	1	1	0	0	0b01111100 or 0x7C
C	0	1	1	1	0	0	1	0b00111001 or 0x39
d	0	0	1	1	1	1	0	0b00011110 or 0x1E
E	1	1	1	1	0	0	1	0b01111001 or 0x79
F	1	1	1	0	0	0	1	0b01110001 or 0x71

 Write code (probably 1 line) to fill in the new bit pattern array that you just designed and paste it below.
DIGIT_PATTERNS = [0b00111111, 0b00000110, 0b01011011, 0b01001111, 0b01100110, 0b01101101, 0b01111101, 0b00000111, 0b01111111, 0b01100111, 0b01110111, 0b01111100, 0b00111001, 0b01011110, 0b01111001, 0b01110001]

## Task 3: Building a Pin Array
Implement the pin array from section 6.4.3 of the computer textbook, or the more sophisticated version from the next (un-numbered) section. Paste your code here.
def setup_dios(pins):
    # Takes a list of pins, returns a list of DigitalInOut objects made from those pins, in the OUTPUT direction.
    dios = []
    for pin in pins:
        dio = digitalio.DigitalInOut(pin)
        dio.direction = digitalio.Direction.OUTPUT
        dios.append(dio)
    return dios
Modify the display subroutine form section 6.4.5 to work with your bit pattern and pin array and paste the code below.
def display(digit, p_array):
if digit < 0 or digit > 9:
return False
pattern = DIGIT_PATTERNS[digit] # See below for the definition of DIGIT_PATTERNS
for idx in range(7):
bit = pattern & 0x01
pins[idx].value = bit
pattern >>= 1
return True

## Task 4: Testing your Subroutine
Next, write a main program that uses calls your subroutine to count from 0 to F on your single digit at a rate of about 5 counts per second. As usual demonstrate the working program, comment the program, and paste the code below.
I lost this program, but hopefully you’ll believe that it existed based on the 2-digit version below.
## Task 5: Extending to 2 Digits
If time permits, connect your second LED display board to another seven I/O pins, write a second routine to write digits to it, and test the whole system with program sketched below, which counts from 00 to FF at about 3 counts per second. You must provide the Display8() function, which will need to split a single 8-bit number into its component nibbles. You may want to review section 6.2 in the computer text.
count = 0
# All your display code goes here
while true:
Display8(count)
count += 1 # Add one to count
time.sleep(0.3)
Paste your working code below and explain how you split the number into two nibbles.
I get the high nibble by shifting right by 4.
I get the low nibble by taking the whole number, and subtracting off high nibble shifted left by 4.
Here’s the program:
# Author: Ben Kallus
# Counts up from 0 to 255 in hex on two 7-segment displays.

import board
import digitalio
import time

PINS_SET_1 = [board.SDA, board.SCL, board.D5, board.D6, board.D9, board.D10, board.D11, board.D12]
PINS_SET_2 = [board.A0, board.A1, board.A2, board.A3, board.A4, board.A5, board.SCK, board.D13]

DIGIT_PATTERNS = [0b00111111,
        0b00000110,
        0b01011011,
        0b01001111,
        0b01100110,
        0b01101101,
        0b01111101,
        0b00000111,
        0b01111111,
        0b01100111,
        0b01110111,
        0b01111100,
        0b00111001,
        0b01011110,
        0b01111001,
        0b01110001]

def setup_dios(pins):
    # Takes a list of pins, returns a list of DigitalInOut objects made from those pins, in the OUTPUT direction.
    dios = []
    for pin in pins:
        dio = digitalio.DigitalInOut(pin)
        dio.direction = digitalio.Direction.OUTPUT
        dios.append(dio)
    return dios

def display_digit(dios, bit_pattern):
    # dios: collection of 8 DigitalInOut objects with the OUTPUT direction, probably connected to a 7-segment display.
    # bit_pattern: The bit pattern to write to the dios.
    # Writes bit_pattern to the dios
    bits = bin(bit_pattern)[2:]
    for i, bit in enumerate(reversed("0" * (8 - len(bits)) + bits)):
        dios[i].value = bool(int(bit))

def display_number(dios_set_1, dios_set_2, number):
    # dios_set_1: collection of 8 DigitalInOut objects with the OUTPUT direction, probably connected to a 7-segment display.
    # dios_set_2: collection of 8 DigitalInOut objects with the OUTPUT direction, probably connected to a 7-segment display.
    # number: 8-bit number to be displayed in hex on the dios.
    # Displays number on the two sets of dios using display_digit.
    display_digit(dios_set_1, DIGIT_PATTERNS[number - (number >> 4) * 16])
    display_digit(dios_set_2, DIGIT_PATTERNS[number >> 4])

def main():
    dios_set_1 = setup_dios(PINS_SET_1)
    dios_set_2 = setup_dios(PINS_SET_2)

    while True:
        for num in range(256):
        display_number(dios_set_1, dios_set_2, num)
        time.sleep(.2)

if __name__ == "__main__":
    main()